Functional Specification Document

Improved Interactive Job Support

Document / Version	Comments	Date	Author
0.1	First draft	04/25/07	Harald Pollinger

# Introduction
<Provide document logistics-related information in the following sections>
The existing Interactive Job Support has several problems, mainly performance problems, security problems and problems with specific architectures.
These problems result from the way how Interactive Jobs are started: On the execution host, a rlogind or rshd is started, and on the client host a rlogin/rsh client is started. This takes a lot of time, the communication between rlogind and rlogin can't be secured and on some architectures, the OS makes it difficult to start a rlogind from the shepherd.
To fix all these problems at a singe blow, it was decided to rewrite the Interactive Job Support and completely get rid of the rlogind/rshd and rlogin/rsh system binaries. Instead, the shepherd should open a pty, directly start the shell in the pty and redirect input and output from/to the shell over network from/to the client.
# Project Overview
## Project aim
The aim of the project is to fix the three main problems of the existing Interactive Job Support - performance problems, security problems and functional problems on specific architecures.
## Project duration
The project is complete when all qrsh, qmake, qtcsh and tight integration and a new to implement "qsub -pty" test in the testsuite run successfully on all architectures.
The targeted release is N1 Grid Engine 6.2 - thus the project can last at most until the code freeze of 6.2.
## Expected benefit
<Explain the new features/functions that make this product different from prior versions. Clearly state the specific versions wherever possible and the relevant functional differences. If this is not a follow-on product, describe the basic functionality that you estimate will differentiate it from competitive offerings. Reference the ARC cases mentioned in section 1.2 rather than including large quantities of material from them. Document problems that will be fixed in the new version of the product based on categorized and prioritized feedback found in customer complaint repositories. See http://productquality.central and drill down into products for examples. >

Table 2.3 – Differentiation from Prior Versions
As-Is	New Version	Fault Code Category	Customer Priority

1. No more problems with rlogind/rshd on specific OS (HP-UX and Interix).
2. A much better performance of the start of Interactive Jobs.
3. A secured communication between the Interactive Job and the client.
4. The current limits of qrsh -inherit instances on a client will be overcome if “-pty no” is requested. (“-pty yes” is limited by the number of available ptys)
## Project Dependencies
<List the dependencies that this product has on any Sun, 3rd party or competitive product offerings for it’s feature/function set survival. Refer to the PRD and PCD for an initial listing of these dependencies. Reference the PLC Product/component (ID/Name) cases for these dependencies.>

Table 2.4 – Project dependencies
Available	Supplier	Product Name	Dependency

# System Architecture

## Enhancement Functions
<Provide a high level architectural description of the feature set of the product.>

## Overall Block Diagram
### qrsh

qrsh

qmaster

execd
shepherd

submits job
sends job to
starts
starts server
communicates over network with

/bin/sh

starts

communicates over stdin/stdout with

In the red frames are the components that are to be modified

1. The user starts "qrsh" on the submit host
2. qrsh reads the configuration from the qmaster and decides to start in new mode.
3. qrsh starts a server
4. qrsh sends a job containing the contact informations of the server to qmaster.
5. The qmaster schedules the job to an execd
6. The execd starts the shepherd
7. The shepherd opens a master pty and a pipe and forks.
8. The child process opens the corresponding slave pty and uses the slave ptys in and out to be it's stdin and stdout. The child process opens the other side of the pipe and uses it as it's stderr.
   The child process then executes the shell.
9. The parent process then can read and write from/to the pty and from the pipe like from files.
10. The parent process connects to the server of qrsh.
11. The parent process starts two threads, one for reading from the pty and the pipe and writing to the qrsh, one for reading from the qrsh and writing to the pty.
12. qrsh waits for a connection to it's server
13. qrsh starts two threads, one for reading from stdin and writing to the shepherd, one for reading from the shepherd and writing to stdout.
14. Now the shell that was started in the child process of the shepherd will output it's welcome message to stdout. This stdout goes into the pty slave, out of the pty master where the parent process of the shepherd reads from it. The parent process of the shepherd sends this output over network to the server of qrsh, which prints it to it's terminals stdout.
    Error messages from the shell are written to the pipe, read from parent process of the shepherd, written over network to the server of qrsh, which prints it to the terminals stdout. Over the network, stderr messages are specially tagged, so they can be distinguished from stdout messages.
    Any input from the user is read by qrsh and sent over the network to the parent process of the shepherd, which writes the data to the pty master, which forwards the data to the pty slave which is the stdin of the shell.
15. When the shell exits or the job (i.e. the child process of the shepherd) gets killed, the qrsh command must exit, also.
16. When the qrsh command gets quitted (by Ctrl-C or by kill), the master process of the shepherd must quit the child process and end the job.
  Note: It was discussed to use the commlib streaming mode to directly redirect the stdin/stdout of the pty to the qrsh (and vice versa). This was dropped because of these reasons:
- There also have to be control messages sent from/to the qrsh (e.g. for Window size changes). If stdin/stdout was redirected over comlib, another connection for the control messages would have been necessary.
- Other communication layers may not support stdin/stdout redirection.
- With 'manually' forwarding input and output, the shepherd could also be used as tee (i.e. write protocols to disk), if this is wanted later.

### qsub -pty

qsub

qmaster

execd
shepherd

submits job
sends job to
starts

/bin/sh

starts

reads/writes stdin/sdtout files to disk

In the red frames are the components that are to be modified

1. The user submits a job with "qsub -pty..."
2. The qmaster schedules the job to an execd
3. The execd starts the shepherd
4. The shepherd opens a master pty and forks.
5. The child process opens the corresponding slave pty and uses the slaveptys in, out and err to be the stdin, stdout and stderr files of the process.
   The child process then executes the user program.
6. When the user program exits or gets killed,the shepherd must end the job (and itself).
7. When the job gets deleted, the user program must be killed.

# Functional Definition
## Performance
Because the startup gets simplified, it is expected that it will take a much shorter time.
The data transport between job and client will be a bit slower, because transport over commlib is a bit more expensive than the rsh protocol - mainly in secured mode.
## Reliability, Availability, Serviceability (RAS)
## Diagnostics
- Error messages on the client terminal and/or in the job accounting.
- Tracing with DPRINTF
## User Experience
## Manufacturing
## Quality Assurance
The existing Testsuite tests for qrsh, qmake, qtcsh and tight integration and a new to implement "qsub -pty" test will ensure the quality.
### qsub -pty Test
- Submit qsub -pty t each architecture with a job that needs pty and ends itself after a while. Provide a stdin file. Use “tty” as test job.
- Wait until job has ended
- Check stdout/stderr files

## Security & Privacy
In a CSP system, security & privacy are covered by the SSL communication of the commlib.
## Migration Path
The old qrsh functionality will work as before, but the new one will be the default.
## Documentation
The changes have to be documented in man pages (qsub, qrsh, DRMAA), Admin Guide, Users Guide and perhaps Installation Guide.
## Installation
## Packaging
<Describe the packaging requirements for the product. The packaging should be capable of supporting the planned global distribution channels (VARs, Direct Sales, OEMs) and shipping containers. For virtual or internet downloadable products, describe how the product will be positioned, listed and highlighted on the relevant web pages.>

## Issues/Risks and Proposed Mitigation
<Identify any significant risks that are known at this time in Table 7. Some risks are already identified in the PRD and represent a good starting point for developing this section.

Estimate the level of risk by assessing its potential impact and the probability of its occurrence. At a minimum, include specific mitigation plans for each risk that has a MH, HM or HH risk rating. These qualitative estimates will be further refined in later Sun PLC Process phases as additional information is gathered.

Identify any potential mitigation plans and owners if they are known at this time.>

Table 4.16 – Risk and Mitigation List
Category	Risk	Impact / (L/M/H)	Probability / (L/M/H)	Mitigation Plan	Owner

Categories: (e.g. Technical, Market, Schedule, Resource and Financial)
Impact: (L) – Low impact; (M) – Medium impact; (H) – High impact
Probability: (L) – Low probability; (M) – Medium probability; (H) – High probability

# Component Descriptions
<List the functional requirements for each product component in the following sections. A general template is listed below that can be modified as needed for each component. Component description templates have been placed in the Appendices for the more common components. The Appendices are organized by relevant product types as listed below:
The below Appendix sections have been cloaked/Hidden please uncloak
the appropiate section(s) and fill in appropiately

- Appendix 8 – Servers, Workstations, Appliances
- Appendix 9 – Disk Storage Systems
- Appendix 10 – Software Products
- Appendix 11 – Networked Products
- Appendix 12 – Graphics, Networking, I/O, Cards (TBD)
- Appendix 13 – Chip related Products
 Refer to the relevant product type categories and cut/paste the appropriate sections below as needed. Sections can be used from any and all sections in the Appendices and should be considered a starting point for generating the optimal functional specification for your particular product.>

## shepherd
### Overview
### Functionality
See 3.2. Block Diagramms
### Interfaces
In the cluster configuration, a “rlogin_daemon builtin” triggers the new mode - the old mode is used else.
### Other Requirements
## qrsh
### Overview
qrsh is now one binary that also contains the functionality for qsh and qlogin. It must be splitted up in three binaries with all common functionality in libraries before the enhancements can be built in.
### Functionality
See 3.2.1 Block Diagram.
### Interfaces
- The “rlogin_daemon builtin” value triggers the new mode - the old mode is used else.
- Option “-pty [yes|no]”.
  Default for “qrsh <no command>” is “-pty yes”, default for “qrsh <command>” is “-pty no”. “qrsh -inherit” inherits the “-pty” option from the 'master' qrsh.
## qsub
### Overview
### Functionality
See 3.2.2. Block Diagram
### Interfaces
- The command line switch “-pty” triggers the new mode.
- Default without “-pty” switch is the old behaviour.
- It would be possible to use “-i stdin -o stdout -e stderr” (“stdin”, “stdout” and “stderr” used as keywords) to redirect the standard streams not to files, but to the users terminal.
  Is there a difference to “qrsh <command>”?
- A new DRMAA attribute “pty”.
## common modules
### pty.c
    - Contains all pty and tty specific functions. Even the fork is located here, because setting up the pty and forking the child process has to be entwined.
    - It provides some pseudo-terminal for the job and functions to set the tty of the qrsh (i.e. that tty the user sees) to a raw mode (i.e. the tty doesn't interpret control characters. On systems that don't provide a pty and/or a raw mode of a tty, this behaviour must be emulated somehow.
    - Takes input data in a memory buffer and provide output data in a memory buffer.
    - Provides functions that wait blocking for input data
    - It must provide signal handlers (and functions to set this signal handlers) for Window size changes, Ctrl-C, ...
- Provides useful error messages
### communication.c
Wraps the commlib
Takes input data in a memory buffer, provides output data in a memory buffer
- Provides functions that wait blocking for input data
- Provides functions to set communication modes
- Provides useful error messages
- Provides functions to send several control messages, interprets this messages
<Provide any additional product specific functional requirements in this section. The Appendices include several product type specific functional requirements. Sections can be used from any and all sections in the Appendices and should be considered a starting point for generating the optimal functional specification for your particular product.>

# Document History and Approvals
<Record the history of changes to the Functional Specification Document using Table 7. The column headers for this table may be revised to suit the particular needs of your product program's document naming conventions. It is required that an entry be made in this table indicating the Date and Version of the FSD that was ARC approved.>

Table 7 – Document History
Dash	Rev	Date	Description of Change	Originator

<Record the ARC Approval of the FSD here. This can be done by copying and pasting the Opinion from the review in this section. This then provides a record that the ARC had reviewed and approved this FSD.>
The following Appendices provide technology specific sample headers that can be used as a starting point for populating the main document. Cut and paste the appropriate sections as needed. If there are additional sections that you believe should be incorporated as a sample header for future versions of this template, please refer them to the SunPLCPTool administrator.

The below Appendix sections have been cloaked/Hidden please uncloak
the appropiate section(s) and fill in appropiately.

The Appendices are organized by relevant product types as listed below:
- Appendix 8 – Servers, Workstations, Appliances
- Appendix 9 – Disk Storage Systems
- Appendix 10 – Software Products
- Appendix 11 – Networked Products
- Appendix 12 – Graphics, Networking, I/O, Cards (TBD
- Appendix 13 – Chip related Products

# Appendix – Appendix #1 Name