Title
RBridges
Networking Summit
James Carlson
Solaris Networking

---
Preso Text Page
Project Overview
IS-IS Routing
  - Link-state protocol like OSPF
  - Routes IPv4 and IPv6
  - Has some advantages over OSPF
Bridging
  - Includes Spanning Tree and RSTP
  - Integrates at MAC layer
RBridges
  - Invented by Radia Perlman; now IETF wg
  - Uses IS-IS instead of STP

---
IS-IS Routing
Just a brief introduction
Runs directly on link layer
  - Not IP; users see it as more secure
Uses TLVs; easier to extend than OSPF
Simpler, non-modal operation
Can run with zero configuration
We're using Quagga

---
Bridging
The part that touches other projects
Includes snoop visibility
Both mac client and driver
L2: below IP but above aggregation
Forwarding learnt from MAC source
Entries just age out over time

---
Current Architecture
VNIC
VNIC
VNIC
VNIC
VNIC
VNIC
NIC
NIC

---
Current Architecture – with bridge
VNIC
VNIC
VNIC
VNIC
VNIC
VNIC
NIC
NIC
Bridge

---
Current Architecture – with packets
VNIC
VNIC
VNIC
VNIC
VNIC
VNIC
NIC
NIC
Bridge

---
New Architecture – internal bridge
VNIC
VNIC
VNIC
VNIC
VNIC
VNIC
Bridge
NIC
NIC

---
New Architecture – layered view
VNIC
Bridge
Aggr
MAC

---
New Architecture – output side
VNIC
Other VNICs, same MAC
Bridge
Same bridge, other MACs
Aggr
MAC

---
New Architecture – input side
VNIC
Other VNICs, same MAC
Bridge
Same bridge, other MACs
Aggr
MAC

---
RBridges
TRILL encapsulation (L2 tunnels)
Use IS-IS to compute TRILL forwarding
MAC learning similar to ordinary bridges
Allows fine control over L2 paths
Can use parallel paths, loops, weighting

---
Overall RBridges Architecture
dladm
bridged
isisd
snoop
libdladm
libscf
librstp
libdlpi
zebrad
/dev/bridgectl
/dev/bridge/name0
AF_TRILL
dld
fs/dev
bridge
sockfs
mac

---
Kernel Bridge Module
bridged
inst_list
bridge_link_t
list
mac
bridge_stream_t
bl_mh
list
bridge_inst_t
bi_links
bi_fwd
array
avl
bi_control
bi_mac
bridge_fwd_t
bf_links
bridge_mac_t
dld
bmac_list
list
bm_mh
mac

---
MAC Changes (part 1)
Don't panic; just 249 lines
Added “snoop only” feature
  - Uses mac_no_active function and mi_disallow_active
Added bridge on/off for MAC instance
  - Uses mac_bridge_set and mac_bridge_clear (similar to mac_vnic_{set,clear})
Added new on/off notification
  - mac_notify_type_t MAC_NOTE_BRIDGE for txinfo changes

---
MAC Changes (part 2)
Added new rx/tx functions analogous to VNIC hooks
  - mac_bridge_tx_get, mac_low_rx_add, mac_bridge_rx, mac_bridge_capab_get
Added references in mac_impl_t
  - mi_bridge_present, mi_bridge_txinfo, mi_bridge_ref, mi_bridge_xmit, mi_bridge_getcapab_fn, mi_bridge_link
Changed receive fanout to include bridge
  - mrf_active boolean becomes mrf_layer, an enum

---
End
RBridges
Networking Summit
James Carlson
  - james.d.carlson@sun.com